## Slide 1: Elastic buckling analysis of a cold-formed steel stud column with open-source shell finite element software
Cristopher D. Moen and Amoke Shabhari
RunToSolve LLC
Wei-Wen Yu International Specialty Conference on Cold-Formed Steel Structures, Madison, Wisconsin
runtosolve.github.io/ICCFSS2026_MoenShabhariStudElasticBuckling

## Slide 2: Shell finite element analysis, in the open
Few modern shell implementations are available for public inspection, and what commercial codes do under the hood is hard to know
A multi-year effort built a trusted, open-source shell capability in Julia, connected to the general-purpose finite element framework Ferrite.jl
Two Mindlin shell elements are now published as packages with elastic and geometric stiffness matrices
  TriShellFiniteElement.jl, a 3-node triangle
  QuadShellFiniteElement.jl, a "4+2" quadrilateral
This talk walks through one eigenbuckling analysis of a common wall stud with holes
Thanks to Sándor Ádány for the shell element formulations and MATLAB reference implementations

## Slide 3: Two flat Mindlin shells, six degrees of freedom per node
Triangle, TriShellFiniteElement.jl
  Constant-strain membrane; Mindlin bending with the Tessler–Hughes shear treatment (mid-side deflections condensed out)
  Shear relaxation 1/(1 + Cs α), Cs = 0.2, calibrated so a simply supported plate converges to k = 4.0
  Hughes–Brezzi drilling stiffness, so folded plates assemble without singular matrices
Quadrilateral, QuadShellFiniteElement.jl
  The "4+2" element of Moen and Ádány: bilinear shape functions plus two bubble functions, condensed at the element level, which relieves in-plane bending stiffness and part of the shear locking
  Same shear relaxation (Cs = 0.1) and drilling term
  Julia matrices reproduce the MATLAB reference to machine precision (a package test)
• Geometric stiffness from the Green–Lagrange membrane strains (Nx, Ny, Nxy and the gradients of all three translations)
• K φ = λ (−Kg) φ, and with a unit reference load the eigenvalue is the buckling load

## Slide 4: A 362S162-33 wall stud with SFIA service holes
Web 3.625 in, flange 1.625 in, lip 0.5 in, design thickness 0.0346 in; E = 29 500 ksi, ν = 0.3
Braced at midheight: Lx = Ly = Lt = 48 in; pinned, warping-free ends; uniform compression, Pref = 1 N
Four 1.5 × 4 in stadium-shaped holes at 12, 36, 60, and 84 in (24 in o.c.); the brace point is 12 in from the nearest holes
Centerline polyline from CrossSectionGeometry.jl: 85 nodes, corner radius 2t, 4 elements per lip, 20 per flange and web, 4 per corner arc
The same polyline goes to CUFSM.jl, so the shell and finite strip analyses share their geometry
(a) 85-node centerline polyline; (b) web mesh around a hole: structured quadrilaterals outside the 150 mm patch, triangles inside it

## Slide 5: Degrees of freedom, boundary conditions, brace
Ends: ux = uy = 0 at every end node, uz and all rotations free
Load: equal and opposite axial nodal forces by tributary centerline length, giving uniform P/A away from ends and holes
Brace: ux = 0 at the two web-flange corners (translation perpendicular to the web and twist), uy = 0 and the axial datum uz = 0 at the web mid-depth node on the symmetry axis, so no prebuckling stress is induced
Two element types, one DofHandler (patch-boundary nodes share dofs)
dh = DofHandler(grid)
sq = SubDofHandler(dh, quad_cells)
ipq = Lagrange{RefQuadrilateral, 1}()
add!(sq, :u, ipq^3); add!(sq, :θ, ipq^3)
st = SubDofHandler(dh, tri_cells)
ipt = Lagrange{RefTriangle, 1}()
add!(st, :u, ipt^3); add!(st, :θ, ipt^3)
close!(dh)
Pinned warping-free ends and the midheight brace
ch = ConstraintHandler(dh)
add!(ch, Dirichlet(:u, end_nodes, # ux = uy = 0
(x, t) -> [0.0, 0.0], [1, 2]))
add!(ch, Dirichlet(:u, brace_corner_nodes, # ux = 0
(x, t) -> [0.0], [1]))
add!(ch, Dirichlet(:u, Set([brace_web_center]), # uy = uz = 0
(x, t) -> [0.0, 0.0], [2, 3]))
close!(ch)

## Slide 6: Pre-buckling stresses and geometric stiffness
One call per package, summed
Kq = QuadShellFiniteElement.assemble_global_Ke!(
allocate_matrix(dh, ch), sq, qr2, qr3,
IP4(), IP6(), E, ν, t; Cs = 0.1)
Kt = TriShellFiniteElement.assemble_global_Ke!(
allocate_matrix(dh, ch), st, qr1, qr3,
IP3(), IP6(), E, ν, t; Cs = 0.2)
K = Kq + Kt; apply!(K, F, ch)
u = K \ F; apply!(u, ch)
σ = membrane_stresses(dh, u, E, ν, t) # element frame
Kg = assemble_Kg(dh, ch, σ, t) # summed, too
• Static problem solved with Julia's sparse direct solver; membrane stresses recovered element by element (one per triangle, four Gauss points per quadrilateral)
• Normalized by P/A: 1.0 in the bulk, about 1.9 in the web strips beside a hole, 1.25 in the flanges at the hole plane, 0.5 just above and below the hole
Pre-buckling longitudinal membrane stress on the web face around a hole, normalized by P/A

## Slide 7: Solving the eigenvalue problem with ARPACK
Implicitly restarted Arnoldi on K⁻¹(−Kg): its largest eigenvalues are the reciprocals of the smallest buckling loads
A perforated member has hundreds of local modes below its distortional and global loads, so the bottom of the spectrum never reaches them
Shift-and-invert with targets from 14 to 60 kN, 40 modes per target, one indefinite factorization and about 20 s each
Every mode is classified automatically: displacement ratio at the hole patches (local at a hole), rigid-body energy fraction (global: weak-axis, strong-axis, torsion), flange-lip versus web-flange corner motion (distortional), else local
Lowest modes: K⁻¹(−Kg), one Cholesky factorization
Kfac = cholesky(Symmetric(K)); tmp = zeros(n)
op!(y, x) = (mul!(tmp, Kg, x); y .= Kfac \ -tmp)
μ, Φ = eigs(LinearMap(op!, n; ismutating = true);
nev = 12, which = :LM)
Pcr = 1 ./ real.(μ) # N, because P_ref = 1 N
Shift-and-invert: modes nearest a target load σ
Mfac = ldlt(Symmetric(K + σ * Kg)) # indefinite
op!(y, x) = (mul!(tmp, Kg, x); y .= Mfac \ -tmp)
ν, V = eigs(LinearMap(op!, n; ismutating = true);
nev = 40, which = :LM)
Pcr = σ .+ 1 ./ real.(ν)

## Slide 8: Finite strip and closed-form reference values
CUFSM.jl, gross section: local minimum 16.14 kN at 70 mm, distortional 37.20 kN at 460 mm
Hole approximations (CeeSectionBuckling.jl, the RunToSolve SFIA evaluation procedure)
  net section through the hole: local 24.88 kN, above the gross value, so the unperforated web governs
  AISI S100 reduced web thickness tr = t(1 − Lh/Lcrd)^(1/3) = 0.807 mm: distortional 37.30 → 35.35 kN
Closed form, KL = 48 in: Pex = 314.6, Pey = 56.9, Pt = 40.0, flexural-torsional 37.89 kN; weighted-average net properties 31.63 kN
Finite strip at one 1219 mm half-wave (section free to distort): 37.17 kN flexural-torsional, 49.58 kN weak-axis flexure

## Slide 9: Shell finite element buckling loads, kN
Buckling mode | 5 mm mesh | 2.5 mm mesh | 5 mm, no holes | Finite strip / analytical
Local, lowest | 15.95 | 16.00 | 15.79 | 16.14 (CUFSM gross)
Local at the holes (web strips) | 20.45 | 20.56 | – | 24.88 (net section)
Distortional, 3 half-waves per segment | 36.51 | 36.38 | 37.37 | 35.35 (reduced t), 37.30 (gross)
Distortional–hole interaction, 5 half-waves | 32.63 | 32.33 | – | –
Global, flexural-torsional | 35.25 | 34.76 | 37.15 | 37.89 (closed form), 37.17 (CUFSM)
Global, weak-axis flexure | 46.74 | 47.70 | 49.58 | 56.93 (Euler), 49.58 (CUFSM mode 2)
Halving the element length changes every load by less than two percent. The lowest mode is local; the governing global mode is flexural-torsional.

## Slide 10: Local modes
Lowest local mode, 15.95 kN: the web buckles between the holes
Lowest mode at a hole, 20.45 kN: the two web strips bow in opposite directions
5 mm mesh (top) and 2.5 mm mesh (bottom) in each figure; color is displacement magnitude

## Slide 11: Distortional and global modes
Lowest distortional mode, 36.51 kN, lower 48 in braced segment: three half-waves per braced segment, the brace plane is a node
Lowest global mode, 35.25 kN, full 96 in member: lateral translation plus twist, one half-wave in each braced segment, the brace at midheight is a node

## Slide 12: Six minutes on a laptop for a quarter-million dofs
Apple M3 Max laptop, sparse factorizations on 7 threads, less than 2 GB of memory
Each shift-and-invert window is one indefinite factorization and about 27 s; the sweep yields about 190 distinct modes between 16 and 65 kN
Julia compiles the packages on first use, roughly a minute per session
Step | 5 mm mesh | 2.5 mm mesh
Degrees of freedom | 247 998 | 509 286
Assemble elastic stiffness | 6 s | 9 s
Static solve | 3 s | 6 s
Assemble geometric stiffness | 2 s | 3 s
Cholesky factorization of K | 10 s | 20 s
12 lowest modes (ARPACK) | 9 s | 18 s
13 shift-and-invert windows, 40 modes each | 356 s | 903 s

## Slide 13: Documentation and validation live on GitHub
Each repository README documents the element mechanics, the calling sequence with Ferrite.jl, and the default parameters; docstrings cover the public functions
The test suites are the validation record. For the triangle:
  element symmetry, rigid body modes, thickness independence
  uniform compression reproducing PL/EA
  simply supported plate converging to k = 4.0, clamped plate to k ≈ 10.07
  buckling load invariant to the orientation of the plate in space
  torsion of flat and folded strips and of a rounded lipped channel reproducing the thin-walled torsion constant within a few percent
For the quadrilateral: element-by-element comparison with the MATLAB reference, plus the plate bending, membrane, and column buckling benchmarks of the earlier paper
Pkg.test() on either package regenerates every number in this list

## Slide 14: Elastic buckling analysis of a cold-formed steel stud column with open-source shell finite element software
Cristopher D. Moen and Amoke Shabhari
RunToSolve LLC
Wei-Wen Yu International Specialty Conference on Cold-Formed Steel Structures, Madison, Wisconsin
runtosolve.github.io/ICCFSS2026_MoenShabhariStudElasticBuckling